## Slide 1
Frequency Co-ordination -for what?
The Agreement
Frequency Co-ordination -Advantages
Frequency Co-ordination -Disadvantages
The Procedure
Administrative Classification of Frequencies
Preferential Frequency Agreements -Advantages
Preferential Frequency Agreements -Disadvantages
Radio Interference
Regional Offices
Further Questions?
Content  click on left mouse button and go through this Introduction by using right or left arrow on your keyboard
Introduction on International
Radio Frequency Co-ordination

## Slide 2: Frequency Co-ordination -for what?
Avoiding radio interference
Agreements for more than 30 years: RR do not meet all practical requirements
Each country obliged to take account of other stations before putting own into operation
Procedures agreed in the Agreement
Bilateral preferential frequency agreements for frontier zones: who can operate what and with which interference ranges (e.g. Bruges 1997, Carcassonne 1993)

## Slide 3: The Agreement
Aim: Optimise spectrum usage by accurate interference field strength calculations
Modification of general parameters, improvement and supplementation of technical provisions, individual restrictions
Establishment of models for computer-aided interference range calculations
Harmonised parameters: Objectively predictable and transparent decisions
Maximum turnaround times
Solid basis for bilateral and multilateral agreements

## Slide 4: Frequency Co-ordination, Ranges

## Slide 5: Frequency Co-ordination - Advantages
Aim: Optimise spectrum usage
Administrations obliged to co-ordinate frequencies before assigning them
Administrations obliged to ensure harmonised application of technical provisions
Quick assignment of preferential frequencies
Transparent decisions through agreed assessment procedures
Quick assessment of interference through data exchange

## Slide 6: Frequency Co-ordination - Disadvantages (1)
Increase in administrative work and costs (complex procedures, longer turnaround times, topographical database)
Detailed input data required from operators (geographical data, antenna parameters)
Complex operational conditions, assignments subject to diverging conditions

## Slide 7: Frequency Co-ordination - Disadvantages (2)
Customers affected by changes in usage rights: Various consequences
Limits also to preferential frequencies, limits may vary from case to case
Use of other countries’ preferential frequencies currently not allowed (restrictions in frequency assignment)
More work in application processing

## Slide 8: The Procedure (1)
Co-ordination request and all technical characteristics of radio network/equipment sent to all administrations affected to enable accurate assessment of interference
Administrations affected assess possibility of interference to own stations; no possibility of interference: obliged to agree to request
If assessments produce different results, administrations can agree to operation on a trial basis; field strength calculations replaced with agreed field strength measurements

## Slide 9: The Procedure (2)
Verification that conditions for preferential frequency use exist and are met (agreement to another country’s use of own preferential frequencies can be refused)
Assessment of border cases: conditional agreement given (NIB/SGNB)
- no interference permitted (NIB)
- no protection against interference from co-ordinated stations (SGNB)
- no interference permitted and no protection

## Slide 10: The Procedure (3)
Administrations draw up and exchange lists of co-ordinated assignments with technical characteristics, administrative reference data, conditions
Aim: basis for co-ordinators’ planning and calculations, validation of assessment results

## Slide 11: Administrative Frequency Classification
Frequencies requiring co-ordination
Preferential frequencies
Frequencies for planned radio networks
Frequencies used on the basis of geographical network plans (same parameters required, e.g. BEL 9Y = 30)

## Slide 12: Preferential Frequency Agreements Advantages (1)
Flexible planning of preferential bands, re-planning possible: very important in particular to public mobile radio networks
Long-term security for preferential frequencies, even if networks not planned or set up until later

## Slide 13: Preferential Frequency Agreements Advantages (2)
Accommodation of totally different transmission techniques (narrowband and broadband) on country’s own preferential frequencies; important if, for example, civil and military services use same band (e.g. C network in D, military services in F)
Shorter turnaround times (time means money)

## Slide 14: Preferential Frequency Agreements Disadvantages (1)
Smaller countries have same amount of spectrum as larger neighbouring countries
Spectrum allocation: 2 countries = 50%, 3 countries = 33.3%, 4 countries = 25%
Other countries’ preferential frequencies cannot normally be used in the defined frontier zones

## Slide 15: Preferential Frequency Agreements Disadvantages (2)
All frequency planning for both non-public and public mobile radio must be in line with each country’s preferential frequency areas in the frontier zones
Preferential frequencies are luxury goods and in great demand
Assignment of non-preferential frequencies is seen as discriminatory because of the required (e.g. operational) restrictions

## Slide 16: Radio Interference Key determining factors (1)
Special protection required?
Co-ordination required?
Calculation of interfering field strength at 10 m on border
Calculation of cross-border interference range according to prediction method, band, etc

## Slide 17: Radio Interference Key determining factors (2)
Consideration of station’s technical characteristics
Consideration of frequency offset and bandwidth of stations affected
Use of specific propagation curves, e.g. CCIR 370-5 (ITU-R P.370-7) (drawn statistically with effective antenna heights)

## Slide 18: Regional Offices Contact Points for Frequency Co-ordination (1)
Often first point of contact for customers requiring radio frequency assignment
Many regional offices in frontier zones and/or in "radio contact" with neighbouring countries, because of topographical conditions
"Inland" regional offices also affected, e.g. CB radio frontier zone regulation
VHF band particularly critical because of possible ranges (e.g. radio amateurs) - foreigners transmit too ...

## Slide 19: Regional Offices Contact Points for Frequency Co-ordination (2)
Operational conditions for frontier zones: participation of Sections 134 and 136
"Simple" frontier zone conditions no longer feasible - more detailed investigation required in future: co-ordination required
Aim: High degree of spectrum efficiency through adherence to VA 93 with little administrative work
Long-term aim: regional office access to central office computer system to enable quick yes/no decision

## Slide 20: Further Questions?
Please contact your National Office*) for International Frequency Co-ordination
*) Find it with a click on the button “Links” on the Homepage of this server